## Slide 1: Pulse Width Modulation (PWM)

## Slide 2: Introduction
Pulse Width Modulation (PWM) has many application in digital communication and power electronics:
  Intensity control of street lights, speed control of dc motor
  PWM is used to generate analog signal from digital signals, digital to analog converter.

## Slide 3: Frequency and Duty Cycle
All waves have the same frequency but different duty-cycle

## Slide 4: Example
50% duty cycle generates 2.5V at the output

## Slide 5: PWM generator in MCU
Software based programming
Hardware based timer counter

## Slide 6: PWM Configuration in STM32
TIM3 – Channel 1
Frequency = 1kHz
  64MHz  1Mhz  1kHz
PA6 is the output of TIM3-CH1

## Slide 7: PWM Programming in STM32
HAL_TIM_PWM_Start(&htim3, TIM_CHANNEL_1);
while (1)
{
__HAL_TIM_SetCompare (&htim3,TIM_CHANNEL_1,10);
HAL_Delay(1000);
__HAL_TIM_SetCompare (&htim3,TIM_CHANNEL_1,100);
HAL_Delay(1000);
}